## Slide 1: WiFi Can Be the Weakest Link of Round Trip Network Latency in the Wild
Changhua Pei†, Youjian Zhao†, Guo Chen†, Ruming Tang†, Yuan Meng†, Minghua Ma†, Ken Ling‡, Dan Pei†
†Tsinghua University ‡Carnegie Mellon University

## Slide 2: WiFi is indispensable in our daily lives!
Promoted by booming of the smartphones:
Mobile offload > cellular in 2015 for the first time
90% of the world’s population over 6 years old will have a mobile phone by 2020. [ERICSSON MOBILITY REPORT JUNE 2015]
Source: Cisco VNI Mobile, 2016
Notes: http://www.statista.com/statistics/292859/north-america-mobile-data-traffic/
Mobile offload exceeded cellular traffic for the first time in 2015
Logic: increase in smartphones -> offload increase in smartphones -> real-time entertainment increase

## Slide 3: WiFi is indispensable in our daily lives!
Booming of the Access Points:
Number of Access Points!
Source: Maravedis, Cisco VNI Mobile, 2016
Notes: http://www.statista.com/statistics/292859/north-america-mobile-data-traffic/
Mobile offload exceeded cellular traffic for the first time in 2015
Logic: increase in smartphones -> offload increase in smartphones -> real-time entertainment increase

## Slide 4
WiFi performance is far from satisfaction
47%
PAGE LOAD TIME
> 3 SECONDS
USES WILL
ABANDON THE PAGES
40%
PAGE LOAD TIME
< 2 SECONDS
USERS
EXPECT
LEADS TO
Akamai study. http://goo.gl/2pwozG.
Notes: INFOCOM 2016 folder delay-value.pdf
http://www-dualstack.akamai.com/html/about/press/releases/2009/press_091409.html

## Slide 5
WiFi performance is far from satisfaction
1
ms
LAST-MILE DELAY
increase
1000
ms
PAGE LOAD TIME
increase
Bismark Paper: S. Sundaresan, N. Feamster, R. Teixeira, N. Magharei, et al. Measur-
ing and mitigating web performance bottlenecks in broadband access
networks. In ACM Internet Measurement Conference, 2013.
Notes: INFOCOM 2016 folder delay-value.pdf
[1] Cisco. Cisco visual networking index: Forecast and methodology, 2013– 2018. CISCO White paper, pages 2013–2018, 2013.
[2] Akamai study. http://goo.gl/2pwozG.

## Slide 6
WiFi performance is far from satisfaction
Stringent Threshold: 20~30ms
Notes: INFOCOM 2016 folder delay-value.pdf
[1] Cisco. Cisco visual networking index: Forecast and methodology, 2013– 2018. CISCO White paper, pages 2013–2018, 2013.
[2] Akamai study. http://goo.gl/2pwozG.

## Slide 7
WiFi performance is far from satisfaction
Unsatisfied
Stringent Threshold: 20~30ms
25ms
Notes: INFOCOM 2016 folder delay-value.pdf
[1] Cisco. Cisco visual networking index: Forecast and methodology, 2013– 2018. CISCO White paper, pages 2013–2018, 2013.
[2] Akamai study. http://goo.gl/2pwozG.

## Slide 8: Challenge 1: Swiping the configurable parameters
Transmit Power?
Channel?
Location?
As large as Possible
1000mw!
1
11
6
Move closer to the AP!
No help to the
RSSI OF CLIENTS
measured on AP.
BLIND SEARCH !
Don’t know what
will happen.
CLIENTS MOVES !
Channel
Width?
Notes: 列出挑战性
But it is hard to reduce the wifi hop latency and there are many chanllenges.
The most common thing people can think up is swiping the configurable …, which including …
People can easily be confused by the blind searching because they don’t know what will happen if they change ….
Besides, increase the transmit power not always works because the transmit power is not equal to the rssi of clients which is measured on AP
And you can not always move the ap close to the clients because the clients always moves.

## Slide 9: Challenge 2: Complex dependencies
Transmit Power?
Channel?
Location?
Channel
Width?
Received signal strength on client-side
Airtime utilization
Packet loss
Transmitting physical rate
Interference
…
Notes: The second hard thing is that there are complex dependencies between different configurable parameters on AP.
We can see in the figure that transmit power will affect the rssi, so is the location.
the channel will affect the airtime utilization , so is channel width.
So how to pick the right parameters to reduce the latency is a tricky things for the AP owners.

## Slide 10: Challenge 3: Trade-off
Channel
Width?
Higher RATE, Higher INTERFERENCE
Lower RATE , Less INTERFERENCE
There isn’t a single rule works for all scenarios!
Notes: The third thing is that , there are many trade-off you must take into consideration when you make the decisions.
We take channel width as a example, if you choose a wider channel, you have larger possiblility to receive the higher
Physical rate, but it will also leads to higher interference. And vice versa
So we can see that it is hard things to tune the parameters at AP to reduce the wifi hop latency, and there isn’t a single rule woks for …
And our wok will focus on this and aim to help the AP owner reduce the wifi hop lantency more easily.

## Slide 11: Our work
Systematic study
Guidelines for optimization
transmit power +10dbm
average latency -10%
Choose another channel
maximum latency -20%
…
…
Notes: In our work, we aimed to provide some optimization guidelines after some systematic study of the AP.
The optimization may like the following two examples.
The first example is that after some studies , we suggest the AP owner increase the …. , and we predict that after this action, the average latency will decrease by 10 percent.
Another example is that user want to decrease the maximum latency by 20%, after diagnose using our system, we find that increase the
Transmit power does not help , but if choose another channel ,it will work.

## Slide 12
…
Airtime Utilization
Retry
Ratio
RSSI
Throughput
Physical
Rate
Queuing
Length
Transmit Power?
Channel?
Location?
Channel
Width?
DELAY
Gap
Model
Domain
Knowledge
Configurable
Parameters
WiFi Factors
WiFi Hop
Latency
Notes: 列出是那些factors
The design principle of our work is simple, to fill the gap between … we continiously measure the WiFi hop factors, which including …
Than we set up the model to predict the wifi hop latency use this wifi factors.
As the relationship between the configurable … and wifi factors is well-studied and clear. We can easily map the wifi factors to the
Configurable parameters and our optimization work in the fillowing pages will show this detailly.

## Slide 13: Predicting the Latency using WiFi factors
…
Machine Learning
WiFi Hop
Latency
WiFi
Factors
Predicting Model
Notes: 列出是那些factors
Because of the large amout of the wifi factors and complex non-linear relationship between factors and latnecy , ml is the ideal tool to predict the wifi hop latency.

## Slide 14: Roadmap
How to accurately measure the WiFi hop latency?
How to predict the WiFi hop latency using WiFi factors effectively?
How to use this model to help AP owners to tune their APs?
Notes: Util now , there are three things we need to do : the first is , the second the last .
We will answer this in the following sections.

## Slide 15: Outline
Introduction
Methodology & Measurement
Analysis& Model
Optimization & Future Work

## Slide 16: Measuring WiFi Hop Latency
Using PING at client side: RTT = t3-t0
Packet Capture:
DL = t3 – t2’
Time synchronization
client-side modification
t0
t1’
t1
t2
t2’
t3
t4’
t4
UL
PL
WL+S
PL
DL
RTT
S
TCP SYN
TCP SYN-ACK
TCP ACK
Client
AP
Server
Notes: Here I first breaking down the round trip time at the view of the WiFi client

## Slide 17: Measuring WiFi Hop Latency: our work
 | Delay Type | Description | 
3-way handshake packets | WL | t2’-t1’ | √
 | DL | t3’-t2’ | √
 | UL | t4’-t3’ | √
Data packets | WL | S | ×
 | DL | t3’-t2’ | √
 | UL | delay-ACK | ×
t0
t1’
t1
t2
t2’
t3
t4’
t4
UL
PL
WL+S
PL
DL
RTT
TCP SYN
TCP SYN-ACK
TCP ACK
t3’
MAC Layer ACK
Use the latest 3-way handshake packet to approximate!
Notes: To measure the DL, we make the driver modifications at the ap side. First we tag the packet when
After the mac layer ack turned back by the client, we will timestap the packet in the callback faction using t3 prime

## Slide 18
Abbreviation | WiFi factors | Description | Generated By
AU | airtime utilization | % of channel time used by all the traffic | iw info
Q | queue length snapshot | Number of packets queued in hardware queue. | debugfs
RR | retry ratio | %packets retried in IEEE 802.11 MAC-layer. | iw info
RSSI | RSSI | Received signal strength of UE associated on AP. | iw info
Ttx | transmitting throughput | Bytes sent to UE every 10s. | ifconfig info
Trx | receiving throughput | Bytes received from UE every 10s. | ifconfig info
RPR | receiving physical rate | Snapshot of physical rate for receiving packets from UE. | iw info
TPR | transmitting physical rate | Snapshot of physical rate for sending packets to UE. | iw info
Notes: These are the wifi factors, which generate by the built-in openwrt

## Slide 19: Data collection
Real deployment in Tsinghua University in China.
47 free Netgear WNDR4300 router equipped with Openwrt
44 in dormitory, 3 in department of computer science
Continuously collected from May 20th to July 20th
Collected about 2 terabytes raw data trace

## Slide 20
Office AP: 50%(10%) packets’
WiFi hop latency > 20ms(100ms)
Notes: The first result we got is … of four overlapping categories

## Slide 21: Rush hour: refer to measurement on Tsinghua campus by our group
Sui, Kaixin, et al. "How bad are the rogues' impact on enterprise 802.11 network performance?." Computer Communications (INFOCOM), 2015 IEEE Conference on. IEEE, 2015.
Department Rush Hour:
16:00-17:00
Dormitory Rush Hour:
23:00-24:00
Notes: The rush hour is refererd to .. Our graph

## Slide 22: Measurement Result
For nearly 50% of the domestic packet, over 60% of the time is occupied by WiFi hop delay.
Domestic occupy over 98% of the whole packets.
Notes: We also calculate the wireless ratio

## Slide 23: Outline
Introduction
Methodology & Measurement
Analysis & Model
Optimization & Future Work

## Slide 24: Visualization of the correlation
Airtime Utilization
Transmitting Physical Rate
Receiving Throughput
Transmitting Throughput
RSSI
Retry Ratio
Queue Snapshot
Receiving Physical Rate
Positive Trends
Negative Trends
No Clear Trends
Notes: We also visualize the correlation between the latency and corresbonding factors.
Generally speaking ,t here are three

## Slide 25: Visualization of the correlation
Airtime Utilization
Transmitting Physical Rate
Receiving Throughput
Transmitting Throughput
RSSI
Retry Ratio
Queue Snapshot
Receiving Physical Rate
Positive Trends
Negative Trends
No Clear Trends
Notes: We also visualize the correlation between the latency and corresbonding factors.
Generally speaking ,t here are three

## Slide 26: Visualization of the correlation
Airtime Utilization
Transmitting Physical Rate
Receiving Throughput
Transmitting Throughput
RSSI
Retry Ratio
Queue Snapshot
Receiving Physical Rate
Positive Trends
Negative Trends
No Clear Trends
No strong effect on WiFi hop latency when :
AU < 0.5 or TPR > 60 Mbps or RSSI > -60 dbm
Notes: Another result we can get is that

## Slide 27: Correlation Analysis
Kendall correlation: (Kendall)
AU has few outliers
Relative Information Gain: (RIG)
how much a factor helps to predict the final latency
Quality Metric | Kendall | RIG
AU | 0.86 | 0.05
RSSI | -0.5 | 0.06
RR | 0.4 | 0.08
TPR | -0.3 | 0.11
RPR | -0.2 | 0.09
Trx | -0.17 | 0.01
Q | 0.15 | 0.007
Ttx | -0.006 | 0.02
Notes: We also give the quatification result of the correlaton， we use
Number of concordant pairs minus number of discordant pairs
Ken’ kao deng te

## Slide 28: Correlation Analysis
  TPR is the best choice to present the latency. This is because of the rate adaption algorithm.
Quality Metric | Kendall | RIG
AU | 0.86 | 0.05
RSSI | -0.5 | 0.06
RR | 0.4 | 0.08
TPR | -0.3 | 0.11
RPR | -0.2 | 0.09
Trx | -0.17 | 0.01
Q | 0.15 | 0.007
Ttx | -0.006 | 0.02
Notes: The second

## Slide 29: Correlation Analysis
Quality Metric | Kendall | RIG
AU | 0.86 | 0.05
RSSI | -0.5 | 0.06
RR | 0.4 | 0.08
TPR | -0.3 | 0.11
RPR | -0.2 | 0.09
Trx | -0.17 | 0.01
Q | 0.15 | 0.007
Ttx | -0.006 | 0.02
  AU is not the best choice (largest RIG) because majority of packets’ AU < 0.5 which does not affect the latency that much.
Notes: We can also see that

## Slide 30: Correlation Analysis
Quality Metric | Kendall | RIG
AU | 0.86 | 0.05
RSSI | -0.5 | 0.06
RR | 0.4 | 0.08
TPR | -0.3 | 0.11
RPR | -0.2 | 0.09
Trx | -0.17 | 0.01
Q | 0.15 | 0.007
Ttx | -0.006 | 0.02
  Q provided by the debugfs is inaccurate, which remind us to use it carefully.
Notes: The last thing we can learn

## Slide 31: Decision Tree
Decision Tree
( AU, RR, RSSI, Trx, Ttx, TPR, RPR)
Predicting Model
SLOW/FAST
Notes: We choose the decision tree to predict the wifi hop latency

## Slide 32: Decision Tree
Package: scikit learn package
Evaluation: 10-fold validation
Notes: We classified the latency into fast and slow categories using stringent threshold

## Slide 33: Decision Tree
DL: Direct measurement
UL/UL+DL: approximating using the latest 3-way handshake packet. (avoid delay-ACK mechanism)
Method | Latency Type | Accuracy | Truth Positive Rate | False Positive Rate
Decision Tree | DL | 0.78 | 0.76 | 0.24
 | UL | 0.68 | 0.67 | 0.27
 | DL+UL | 0.77 | 0.79 | 0.31
Notes: This is the accuracy evaluation of our model

## Slide 34: Decision Tree
The Random Forest, ( tree number = 200, tree depth = 100), Accuracy > 0.8 with 0.21 False Positive Rate for DL.
Why Decision Tree instead of Random Forest?
interpretability + usability
Method | Latency Type | Accuracy | Truth Positive Rate | False Positive Rate
Decision Tree | DL | 0.78 | 0.76 | 0.24
 | UL | 0.68 | 0.67 | 0.27
 | DL+UL | 0.77 | 0.79 | 0.31
Notes: We also try the random forest as comparision

## Slide 35: Decision Tree
Notes: We tune the tree into six layers and we use this in the following optimization

## Slide 36: Outline
Introduction
Methodology & Measurement
Analysis& Model
Optimization & Future Work

## Slide 37: Three Steps for Optimization
Collect raw trace from the AP we want to diagnose and input them to the decision tree
Find the slow branch and locate the candidate for optimization.
Reconfigure the AP to change the value of certain split criterion.
Notes: Here I first introduce the tree steps for optimization
1. Collect raw trace which contains WiFi factors which we want to diagnose and input them to the decision tree
2. Find the slow branch which has the largest number of samples. Trace the path to root of the tree, every split parameter can be potential candidate for optimization.

## Slide 38: Case Study 1
TPR = 54Mbps
AU = 0.6
RSSI = -45
RR = 0.5
RPR = 6Mbps
TPR = 6 Mbps
AU = 0.3
RSSI = -45
RR = 0.5
RPR = 6Mbps
> 78Mbps
> 68Mbps
branch | B1 | B2 | B5 | B6 | B7 | B10 | B11 | B12 | b13
before |  |  |  |  |  |  |  |  | 
after |  |  |  |  |  |  |  |  | 
0.1%
0.8%
3%
58%
0
6.7%
13.4%
4.2%
13.8%
0%
0%
0
0.5%
61.2
0.4%
3.5%
0.4%
34%
Notes: The first optimization is done on AP in the department which has high wifi latency all the day-time.
First we collect the trace and classify the trace as this two packets show. We do the same thing to other samples. The overall result show as follows
We find that

## Slide 39
Case Study 1: Relocate the AP
CDF of OAP DL one week before and one week after optimization under the guidance of decision tree.
50ms
10ms
5X improvement!
Notes: We draw the dl 1 week before and after the optimization

## Slide 40
Case Study 2: Channel Switching
Notes: Tree steps
The second optimization is done on the AP, whose user complain

## Slide 41
Case Study 2: Channel Switching
CDF of AU and DL one week before and one week after the channel selection.
0.6
0.52
250ms
50ms
Notes: Tree steps
双向的箭头

## Slide 42: Conclusion & Future Work
WiLy, which effectively breaks down the Round Trip Network Latency for the first time. NO client-side modification, OpenWrt-compatible.
Exhaustive measurement on 47 APs in the wild for two months
Provide a decision tree based model which can be used to diagnose the performance degradation and the optimization show good result.
This work can be further extended by: Delay ACK filtering, applying to dynamic channel selection …
Notes: Propose a method called WiLy, which effectively breaks down the Round Trip Network Latency for the first time. Need not client-side modification. Can be deployed to any OpenWrt-compatible APs.
Present systematic study based on an exhaustive measurement on 47 APs in the wild for two months and present some interesting results.
Provide a decision tree based model which can be used to diagnose the performance degradation. The model show the most important factors and the optimization show good result.
This work can be further extended by: Delay ACK filtering, applying to dynamic channel selection, or more advanced machine learning method.

## Slide 43
Thank you!
peich14@mails.Tsinghua.edu.cn
Notes: 需要亮点比较明确，主题突出。ppt要尽量能够做到colorful

## Slide 44: Abandoned pages
Figures in parentheses refer to 2015,2020 device share
Source: Cisco CNI Mobile,2016
The projected compound annual growth rate (CAGR)

## Slide 45
Source: Cisco VNI Mobile, 2016
IP Traffic by Access Technology

## Slide 46
Notes: https://www.sandvine.com/downloads/general/global-internet-phenomena/2013/sandvine-global-internet-phenomena-report-1h-2013.pdf

## Slide 47: Possible questions:
Why the accuracy is so low?

## Slide 48: Many delay sensitive applications!
    Sandvine 1H 2012 Report
Real-Time Entertainment!
Notes: Mainly refer to the imc2013 dhcp paper:
Configuring DHCP Leases in the Smartphone Era
Important thing: whether the mobile traffic including the WiFi traffic? Does all the traffic generated on the Mobile devices is called Mobile traffic? It is better to find the portion of all traffic, not only mobile traffic

## Slide 49: Gap between parameters and factors
…
Airtime Utilization
Retry
Ratio
RSSI
Throughput
Physical
Rate
Queuing
Length
Challenge: Metrics used to represent the current context/WiFi environment.
Transmit
Power
Channel
Channel
Width
Location
Notes: 列出是那些factors

## Slide 50: Parameter-to-parameter dependencies
…
Channel
Width?
Higher RATE, Higher RETRY
Lower RATE , Less RETRY
Notes: 列出是那些factors

## Slide 51: Three-way handshake packets
For all packets
  PL is negligible
For three-way handshake packets
  No delay-ack:
  S is negligible
WL = t2’-t1’
UL = t4’- t2’ - DL

## Slide 52: Measuring WiFi Hop Latency
User
Equipment
AP
Wireless
NIC
mon0
t1’
t2
MAC ACK
t3’
-